REGION IV REGIONAL RESPONSE TEAM

GUIDANCE FOR

OCEANING DUMPING

DURING POLLUTION RESPONSE ACTIONS

Revised:  January 5, 2002

Introduction

Federal On-Scene Coordinators (OSC) and Unified Commands (UC) responding to pollution or the threat of pollution in the ocean and coastal water environment have been confronted either by limited disposal options or technology constraints when determining the final disposition of a stricken vessel or its cargo.  The goal of the OSC/UC has always been and always will be to identify a means to disposal of a vessel and its cargo in accordance with conventional/routine disposal methods.  However, there are times in the interest of minimizing the impacts to human health, welfare, and safety and the environment that emergency provisions for disposal may be required.   After other disposal alternatives are investigated and found not to be acceptable to the OSC/UC, disposal at sea or “ocean dumping” may be requested.

This document provides Region IV Regional Response Team (RRT) guidance and decision-making tools to support and assist OSC/UC actions within the region when they are pursuing emergency ocean dumping permission to mitigate pollution or the threat of pollution when other conventional disposal methods are not viable.  The information contained within this document was developed strictly to identify issues and provide consistent viewpoints and procedures to assist the OSC/UC and alleviate potential barriers that may inhibit the decision and permit process.  This is a planning and preparedness effort and we encourage Area Committee members to incorporate concepts and information from this document into their respective Area Contingency Plans.   This document is structured into four sections.

- Section I defines the purpose, authority, and scope of the process;

- Section II contains a decision tree for supporting a request for an emergency ocean dumping permit from the U.S. Environmental Protection Agency (EPA);

- Section III contains a decision checklist for emergency ocean dumping permits; and

- Section IV contains a sample emergency ocean dumping permit request letter.

Section I

## Purpose

The purpose of this guidance is to support and enhance the OSC/UC’s ability to quickly determine the best course of action to obtain an emergency ocean dumping permit, if needed, from the EPA to support emergency removal actions under the National Oil and Hazardous Substances Pollution Contingency Plan (NCP) (40 CFR 300).  This guidance outlines the decision-making process, identifies issues, suggests procedures, and provides checklists to help standardize the permit process.  This guidance is a planning and preparedness tool that can be taken in part or in whole and incorporated into various Area Contingency Plans.

As mentioned earlier, the identification of conventional disposal methods and techniques to support the mitigation of a pollution event is the desired objective and is an OSC/UC decision.  No RRT concurrence or consultation is necessary unless the OSC/UC needs the RRT’s support to assist with this process.  However, the RRT recognizes that in some instances the disposal of vessels, cargo, and other materials to support various phases of an OSC/UC response to a significant oil spill or hazardous substance incident is an increasing challenge.  These guidelines were developed to allow the Federal On-Scene Coordinator and their commonwealth/territory On-Scene Coordinator partners, within the Unified Command, to employ concepts or tools from this guidance to help or assist in the pursuit of an ocean dumping permit to:

- Prevent or substantially reduce a hazard to human life;

- Minimize the environmental impact of spilled oil or hazardous substances; or

- Reduce or eliminate economic or aesthetic losses, which would otherwise presumably occur without the use of available resources.

## Authority

There are two issues that confront the OSC/UC when engaged in emergency pollution response/removal or salvage actions when conventional disposal methods for the vessel, its cargo, and other materials are not feasible.

- Transportation and Disposal of Vessels.   General permit provisions provided within 40 CFR 229 adequately allow for the transportation and disposal of vessels in emergency situations.  The process is clear and will not be further discussed within this document.

- Disposal of Cargo and Other Materials.  Emergency permits are addressed in the ocean dumping regulations a 40 CFR 220.3(c), which provides:

- A permit may be issued to dump materials where substances prohibited as other than trace contaminants are present in greater than trace amounts:

- after consultation with the Department of State, to determine if any of the signatories to the Convention on the Prevention of Marine Pollution by Dumping of Wastes and Other Matter (the London Convention of 1972) are likely to be affected by the emergency dumping: and

- when an emergency has been demonstrated to exist that requires such dumping.  The emergency must pose an unacceptable risk relating to human health, and admit of no other feasible solution.  As used in 40 CFR 220.3(c), “emergency” refers to situations requiring action with a marked degree of urgency, but is not limited to circumstances that require immediate action.

- Emergency permits may be issued for other materials, except those prohibited by 40 CFR 227.5, without consultation with the Department of State, when EPA determines that there exists an emergency requiring the dumping of such materials, which poses an unacceptable risk to human health and admits of no other feasible solution.

- Article V(2) of the London Convention of 1972 (LC 72) allows the issuance of emergency permits as an exception to LC 72 Article IV(1)(a) and Annex I prohibitions against the dumping of certain substances.  40 CFR 220.3(c) implements the provisions of that article.  Consistent with LC 72 Article V(2), 40 CFR 220.3(c) is intended to assure that necessary consultation with the International Maritime Organization and potentially affected states take place if the material to be dumped contains greater than trace contaminants of LC 72 Annex I substances.  LC 72 Annex I constituents are listed in 40 CFR 227.6.

## Scope of Process

This guidance outlines the process to pursue a ocean dumping permit from EPA when no other suitable alternative dumping arrangements can be identified.

- Alternative Dumping Arrangements.  The OSC/UC must pursue the identification of suitable alternative dumping options prior to seeking an ocean dumping permit.  Landside disposal options, including recycling, landfill disposal and storage, or other conventional methods must be investigated for the subject material and determined to be infeasible due to logistical considerations and the immediacy of the threat.

- State Restrictions.  The states may place additional restrictions on ocean dumping in State waters.

- Human Health Risk.  The OSC/UC must document or identify the unacceptable risk to human health that the urgency of the situation poses.  This threat should illustrate that the risk to human health requires, in the public’s interest, the issuance of an emergency permit as soon as possible.

- Emergency Ocean Dumping Permit Request Critiera.  The following issues should be addressed and documented within the OSC/UC permit request:

- Background synopsis of the incident focusing on the operational need to mitigate the event and the proposed solution including a discussion on the proposal for ocean dumping of cargo or other materials.

- The inability of the OSC/UC to identify an alternative dumping arrangement suitable and feasible to support the operation given the existing threat.  Included within this discussion should be the type of material involved in the permit request, the quantity proposed for dumping, and the proposed location of the dumping.

- The risk to human health should the permit not be granted.  Also mention supporting threat issues such as inhibiting navigation, archeological/cultural resource protection, ecological/sensitive wildlife, etc.

Section II

Decision Tree for Requesting an Emergency Ocean Dumping Permit

The decision tree for supporting a request for an emergency ocean dumping permit is as follows.  The flowchart follows the various steps and decision-making needed to request a permit.  The process addresses the following high points in the process:

- Search for alternative dumping/disposal options;

- Inquire as to any additional restrictions by the applicable State in areas where they have jurisdiction;

- The risk or threat to human health;

- RRT support available to process the request;

- Verbal contact with EPA Division of Environmental Planning and Protection to discuss the permit request; and

- OSC/UC forwarding of the request through the Seventh Coast Guard District Chief, Marine Safety Division to EPA.

#### EMERGENCY OCEAN DUMPING PERMIT DECISION TREE

Disposal options may include:

Landside disposal;

Recycling;

Landfill disposal/storage; or

Other conventional methods

Yes

No

Other Associated Risks:

No	  Navigation threat

Archeological/cultural resources

Ecological/sensitive wildlife

Economic impacts

Other affects on the port/area

Yes

OSC/UC request contains:

No	  Synopsis of the incident

Inability to ID suitable alternative

dumping arrangements

The risk to human health

Addresses any State Restrictions

Operational details

Yes

Section III

Decision checklist for an emergency ocean dumping permit follows.  The checklist is separated into four (04) steps.

- Step 1 – Spill, Pollutant, and Environmental Background Information

- Step 2 – Alternative Dumping/Disposal Options

- Step 3 – Human Health and Other Associated Risks

- Step 4 – Emergency Ocean Dumping Permit Request

Each step allows the user to address and check-off each of the issues presented within the  “Emergency Ocean Dumping Permit Decision Tree”.  Additionally, the checklist provides points of contact and other amplifying information to streamline the process for the Federal OSC and Unified Command.

NOTE:  This checklist is designed as a job aid or tool to assist you through the permit request process.  The information provided within the checklist was intended to provide you with sufficient background on the subject so the checklist would be helpful when separated from other portions of this guidance document.  This tool was developed to help quicken your efforts and not hinder the process.  There may be portions of the checklist that are not applicable to your specific incident or the user may not need to complete each portion of the checklist to sufficiently meet the objectives of the permit request process.  Use the tool to your best advantage in whole or in part.

Emergency Ocean Dumping Permit Operational Checklist

Step 1:  Spill, Pollutant, and Environment Background Information

General Information:

- Name of Incident:  _________________________________________________________________

- Unified Command Location:  _________________________________________________________

C.  Responsible Party (if known):  ________________________________________________________

D.  Date and Time of the Incident:  ________________________________________________________

- Type of Incident:  (check all that apply)

_____	Vessel Grounding

_____	Vessel Fire

_____	Facility Incident

_____	Tank Truck Incident

_____	Transfer Operation (Vessel, Facility, Truck, or Pipeline)

_____	Explosion

_____	Vehicle Accident

_____	Blowout

_____	Pipeline

_____	Mystery

_____	Pollution Involved or Threatened

_____	Other:  _______________________________________

F.  Spill Location: 	____________________________________________________________________

____________________________________________________________________

G.  Distance and Direction to nearest human use areas (e.g., schools, hospitals, recreation areas, surface water intakes, public wells, channels, harbors, etc.):

Area	Distance	Direction

______________________________________	_______	_______

______________________________________	_______	_______

______________________________________	_______

______________________________________	_______	_______

______________________________________	_______	_______

Pollutant/Oil Information:

H.  Product(s) Released:	_____	Heavy Crude

_____	Bunker C/#6 Fuel Oil

_____	Medium Crude

_____	Diesel/#2 Fuel Oil

_____	Jet Fuels

_____	Gasoline

_____	Other (please specify):  ____________________________________

I.  Product Details:	Product Name: 	_____________________________

Viscosity:	_____________________________

API Gravity:	_____________________________

Pour Point: 	_____________________________

Percent Evaporation in: 	24 Hours - __________  48 Hours - ___________

J.  	Estimated Volume of Released oil:	_______________ gals  ______________ bbls

K. 	Estimated Volume of oil potentially released:	_______________ gals  ______________ bbls

L.	Release Status:  _______ Continuous  ________ Intermittent

One Time Only, Now Stopped?  Yes _____  No _____

If Continuous or Intermittent, Specify Rate of Release:  ________________gals/bbls per hour

- Estimated Surface Area Covered:  _______________ acres/sqft

Cargo Information:

N.  Cargo Type:	_____	Bulk Oil

_____	Bulk Liquid Hazardous Substance

_____	Dry Bulk

_____	Containerized

_____	Other (please specify):  ____________________________________

O.  Product Details:	Product Name: 	_____________________________

P.  	Estimated Volume of Cargo Released or Threatened to Release:	_______________  units _____

Q. 	Estimated Volume of Cargo Potentially Released:	_______________ units  _____

R.	Release Status:  _______ Continuous  ________ Intermittent

One Time Only, Now Stopped?  Yes _____  No _____

If Continuous or Intermittent, Specify Rate of Release:  ________________units per hour

- Estimated Surface Area Covered:  _______________ acres/sqft

Environment Information:

T.	Current Weather: 	_____	Clear

_____	Partly Cloudy

_____	Overcast

_____	Rain/Snow/Fog

_____	Inversion

24 – Hour Projection: 	_______________________________________________________________

48 – Hour Projection:	_______________________________________________________________

Wind Speed:

Surface	Forecasted

Current Wind Speed (mph):	_______	________

Direction (from):		_______	________

24-Hour Projection (mph):	_______	________

Direction (from):		_______	________

48-Hour Projection (mph):	_______	________

Direction (from):		_______	________

Note:  Any information from visual overflights of the slick, including estimations of slick thickness, should be included here.  All additional available information pertaining to physical characterization of spilled oil should be included here.

Step 2:  Alternative Dumping/Disposal Options

Identification of Cargo and/or Other Materials for Dumping/Disposal:

A.	Cargo and or other materials to be disposed of:

Material Name:  ____________________________________  Quantity:  _______________

Material Name:  ____________________________________  Quantity:  _______________
 	Material Name:  ____________________________________  Quantity:  _______________
 	Material Name:  ____________________________________  Quantity:  _______________
 	Material Name:  ____________________________________  Quantity:  _______________

Identification of Dumping/Disposal Options:

B.	Dumping and disposal options investigated by the OSC/UC:
	
 		_____	Landside Disposal

_____	Recycling

_____	Landfill Disposal/Storage

_____	Other Conventional Methods (please specify):  __________________

_______________________________________________________

C.	Has the OSC/UC identified a suitable dumping/disposal option given the operational constraints or windows of opportunity of the response action?

- Yes  ( if yes, use the selected disposal option) 

 	No   (if no, continue with Step 3)

Step 3:  Human Health and Other Associated Risks

A.	Has the OSC/UC determined that if the cargo and/or other materials are not disposed of within the established window of opportunity a human health risk is present?

	Yes  (if yes, explain)

  	No   (if no, do not proceed with permit request)

- What is the human health risk?
________________________________________________________________________________
________________________________________________________________________________
________________________________________________________________________________
________________________________________________________________________________
________________________________________________________________________________

C.	What are other risks associated with a failure to expedite the disposal process?

  		_____	Threat to navigation

_____	Archeological/cultural resource protection

_____	Ecological/sensitive wildlife impact

_____	Economic impact

_____	Other (please specify):  ____________________________________

_______________________________________________________

D.	Other issues that need to be considered about the potential dump site.

_____	Projected travel of any potential contaminants

_____	Are there any endangered species in the area

_____	The biological community that may be impacted

_____	Are the waters near a State or National Park, Preserve, or Refuge

_____	Distance to shore

_____	Recreational uses of the area

Step 4:  Emergency Ocean Dumping Permit Request

OSC/Unified Command Ocean Dump Determination:

A.	An Emergency Ocean Dumping Permit to dispose of cargo and/or other materials must be obtained through the U.S. Environmental Protection Agency (USEPA).  Emergency permits are addressed in the ocean dumping regulations 40 CFR 220.3(c), which provides:

- A permit may be issued to dump materials where substances prohibited as other than trace contaminants are present in greater than trace amounts:

- after consultation with the Department of State, to determine if any of the signatories to the Convention on the Prevention of Marine Pollution by Dumping of Wastes and Other Matter (the London Convention of 1972) are likely to be affected by the emergency dumping: and

- when an emergency has been demonstrated to exist that requires such dumping.  The emergency must pose an unacceptable risk relating to human health, and admit of no other feasible solution.  As used in 40 CFR 220.3(c), “emergency” refers to situations requiring action with a marked degree of urgency, but is not limited to circumstances that require immediate action.

- Emergency permits may be issued for other materials, except those prohibited by 40 CFR 227.5, without consultation with the Department of State, when EPA determines that there exists an emergency requiring the dumping of such materials, which poses an unacceptable risk to human health and admits of no other feasible solution.

- Article V(2) of the London Convention of 1972 (LC 72) allows the issuance of emergency permits as an exception to LC 72 Article IV(1)(a) and Annex I prohibitions against the dumping of certain substances.  40 CFR 220.3(c) implements the provisions of that article.  Consistent with LC 72 Article V(2), 40 CFR 220.3(c) is intended to assure that necessary consultation with the International Maritime Organization and potentially affected states take place if the material to be dumped contains greater than trace contaminants of LC 72 Annex I substances.  LC 72 Annex I constituents are listed in 40 CFR 227.6.

- Has the OSC/Unified Command decided to pursue an ocean dumping permit for the USEPA?

Yes  (if yes, explain why below)

  	No   (if no, pursue other conventional disposal methods)

C.	What are the recommended disposal sites offshore (if known)?

Recommended Disposal Site:

Location (Coordinates):  ________________ N  _________________ W

Depth of Water:  ______________________  (units) _______

Location (Coordinates):  ________________ N  _________________ W

Depth of Water:  ______________________  (units) _______

Any Significant Water Current Information:   No ____  Yes (Explain)  ________________________

_______________________________________________________________________________

Emergency Ocean Dumping Permit Request Development:

D. 	Has the Unified Command addressed the following issues within request?   

  	Yes   (if yes, continue checklist.)

 	No    (if no, review steps and obtain desire information.)

E.	Permit Request Content:

Synopsis of the incident;

Inability to identify suitable alternative dumping/disposal options;

Any State restrictions that are applicable;

Risk to human health;

Other associated risks; and

Operational details (material type, quantity, proposed location, etc.)

Communications:

F.	Has the OSC/UC, working through the Coast Guard District Marine Safety and Legal staff, verbally communicated with USEPA?  

 	 	Yes    (if, yes, proceed)

 		No     (If no, please make contact…may use the District to do this for the OSC/UC)

G. 	U.S. EPA Contacts for federal Region IV:

Primary Contact:	Chief, Emergency Response and Removal Branch
RRT Support 	U.S. Environmental Protection Agency, Region IV
 	61 Forsyth Street, 11th Floor
 	Atlanta, GA  30303
 	
  	Tel:  	    (404) 562-8721
  	Fax:          (404) 562-8699
  	24 hr:        (404) 562-8700

Permit Request Processing:

H. 	Has the OSC/UC forwarded the permit request to the Seventh Coast Guard District?
 
 		Yes    (if, yes, proceed)

 		No     (If no, please forward request)

I.	Seventh Coast Guard District contacts:

 		Marine Safety Division:  	Tel – 	(305) 415-6860
  		 	Fax -	(305) 415-6875

Legal Staff:	Tel – (305) 415-6954/6958/6957

  		Commander (m)
 		Seventh Coast Guard District
  		909 SE First Avenue
  		Brickell Plaza Federal Building, Room 808
  		Miami, FL  33131-3050

J.	The OSC/UC drafts the permit request and forwards the same to the Seventh Coast Guard District Marine Safety staff.  A sample request letter is contained within Section IV of this guidance document.

K. 	Emergency Ocean Dumping Permit request is forwarded by the Seventh Coast Guard District Marine Safety staff after consult with District Legal to the U.S. EPA.

Section IV

Emergency Ocean Dumping Permit Request Sample Letter

The following document is a sample permit request letter that can be used as a tool to complete the final step of the proceeding checklist.   The letter should at a minimum include the following criteria specified within the request development portion of Step 4.

- Synopsis of the incident;

- Inability to identify suitable alternative dumping/disposal options;

- Any additional restrictions by the State in areas where they have jurisdiction;

- The risk to human health;

- Other associated risks; and

- Operational details (material type, quantity, proposed location, etc.).

# Text boxes

OSC/UC determines that cargo and/or other materials from a stricken vessel needs to be lightered & disposed

OSC/UC determines that ocean dumping of cargo and/or other materials from lightering operations is the only viable option

OSC/UC uses disposal method for final disposition of lightered materials or cargo

USCG D7m forwards request to USEPA

OSC/UC disposes of cargo and/or other materials in accordance with the USEPA Permit

USEPA approves the request and grants the ocean dumping permit

OSC/UC submits a request for a ocean dumping permit to USEPA via USCG D7m

OSC/UC determines that an unacceptable risk to human health exists

OSC/UC identifies a suitable conventional disposal method

OSC/UC pursues the identification of suitable conventional disposal options