## Slide 1: CSX Hazmat Response
2023

## Slide 2
Presenter
Ryan Godsey / James Courtney
Introduction

## Slide 3: CSX Network
  Approximately 21,000 route miles across 26 states, including the District of Columbia
  Most advanced intermodal terminals in North America
  Connection to 240+ short line partners and 70+ port terminals
  Reliable service with transparency through Trip Plans
CSX Network Reaches Nearly Two-thirds of the U.S. Population
# OF EMPLOYEES
22,500+
CARLOADS
3.3M
CAPITAL INVESTMENT
~$1.8B

## Slide 4: Common carrier Obligation
Key Takeaways
The safest way to move hazmat over land, freight railroads are legally required to transport this commodity under a common carrier obligation
  Safety efforts have significantly decreased the hazmat accident rate
  Railroads have limited control over hazmat transportation decisions
  True costs and risks are not fully reflected in shipping rates
Railroads move large quantities of Hazmat, including fertilizers, ethanol, crude oil, refined petroleum and chlorine
  Railroad has invested enormous resources to ensure the movement is safe
  Aspirations to eliminate accidents and incidents altogether
  More than 99.9% of all hazmat reaches its destination without incident.
  Source: Association of American Railroads
Notes: Loads of Chlorine and Ammonia are fewer and fewer each yard
94% of accidents involving hazardous material are on the highway

## Slide 5: Top 20 Hazmat Materials Moved on CSX Network

## Slide 6: Preparedness
Hazardous Materials Team
11 Hazardous Materials Managers
  Actively engages with first responders, emergency managers, and regulatory authorities to perform training & outreach
  Respond to incidents
  Hazmat railcar compliance
  Engage with customers
3 Chemical Safety and Preparedness & Training Managers
  “Behind-the-scenes”
  Support field-managers
  Manage training assets and programs
  Regulatory compliance
Notes: Photo is of Lynchburg, VA 2015

## Slide 7: Preparedness
Industrial Hygiene Team
Work with Hazmat Team for TestNet Air Monitoring and Tech Support
    Annual training with TestNet contractors
Team is designed to be scalable
Under ICS – Safety Officer (can work parallel with Coast Guard)
    Work in tandem with Site Safety Officers
    Manages Health and Safety Plans
Prepared to deploy and manage 3rd party Air Monitoring / Toxicology support
    Monitor the worksite and community, when needed

## Slide 8: Preparedness
Risk Management Team
24 Field Managers
On-call 24/7
Respond to:
  Crossing accidents
  Trespasser strikes
  Derailments and crisis situations
Notes: Photo is of Lynchburg, VA 2015

## Slide 9: Response
Public Safety Coordination Center (PSCC)
800-232-0144 x1 (emergencies)
Initial POC for all railroad personnel & First Responders
Can shut down tracks / Alert Train Dispatchers
Coordinates information sharing among:
    Train Dispatchers
    911 Operators
    First On-scene Personnel
    CSX Hazmat Team
    CSX Risk Management Team
    CSX Corporate Communications
  Can provide Train Consist & Car info

## Slide 10: Response
Local First Responders
  CSX PSCC / Local 911
    Will typically get notified first by train dispatchers or citizens
  Local 9-1-1
    Initiates local responders
    Notifies the railroad
  PSCC
    Gathers any available train information / documentation
    Notifies Local 9-1-1
    Can provide train consist / standing order
    Makes initial internal notifications

## Slide 11: Response
  CSX PSCC can provide 911 dispatch with train and car info
  Can be Emailed or Faxed
  Consist
  Electronic record, most recent wheel report of cars & positions in train
  Identifies HazMat and safety info
  Standing Order
  Easy to read list of what is on the train
  Lacks HazMat details provided in the consist
Train Documents
Notes: Consist:
Page 1 – Introduces Train ID, Locomotive ID’s, with DP Loco at position 112, How to tell if loaded/empty, how to identify HM cars
Page 2 – Shows again how to tell if cars are loaded/empty and HM or not. How many loaded/empty cars in consist, and total cars in train
Page 3 – CT 168 report, Key field codes, and shows every HM car and location on the train. Review position revision area
Page 4 – Block summary with Hazmat commodity info for each car
Page 5 – Hazmat Special Handling Instructions for each type of hazmat on the train
Page 6 – Illustrates how there is more than one car carrying the same commodity, and it’s position in train.
Standing Order
Page 1 – Shows basic info in a spreadsheet form
Page 2 – How to identify Hazmat cars among all the others
Page 3 – How to identify a non-haz tank car

## Slide 12: Response
  CSX Hazardous Materials Team
  Training Qualifications
    Minimum of Hazmat Technician
    Chemical Specific Training
    Chemistry of Hazmat Materials (VDEM)
    Advanced Leak and Spill (VDEM)
    Tank-Car Specialists
  Field Managers
    Respond to emergencies
    Provide Training
    Participate in an LEPC
    Assist with pre-planning and checklists

## Slide 13: Response
  CSX Hazardous Materials Team
  Equipment carried on-hand
    Responder Vehicles
    Turnout Gear, SCBA, other PPE
    Thermal Imaging Cameras, Radiation Detectors, 4-gas meters w/ PID, & Color Metric Tubes
    Tank Car Manway Gaskets
    Partial Midland Kits
    Various Tank Car Tools and Materials
  MoCC (Mobile Coordination Center)

## Slide 14: Response
  CSX Hazardous Materials Team
  MoCC (Mobile Coordination Center)
    2 Conference Rooms,
    18 Individual Work Areas
    Mapping Printer
    Radio Bays
    Satellite and Cell Internet & Communications Suite
    Housed in Winston-Salem, NC
      Can be mobilized in under 4 hours
        Never had to wait that long

## Slide 15: Response
CSX Industrial Hygiene Team
  Training Qualifications
    Minimum of Hazmat Technician
    Air Monitoring / Air Sampling
    Certified Industrial Hygienists & Health and Safety Professionals
  Equipment carried on-hand
    Hand-held direct reading instruments
    AreaRae direct reading instrument
    FTIR (“Gasmet” brand Google image),
    Various air monitoring & sampling capabilities available
  Immediately gather SDS for any involved chemicals
    For use and development of Health & Safety Plan and Air Monitoring Plan
  Avg Response Times, 4< hours

## Slide 16: Response
CSX Industrial Hygiene Team

## Slide 17: Response
CSX Environmental Remediation Team
  Training Qualifications
    OSHA 40 hr Hazwoper
    RCRA Hazardous Waste Training
  Equipment carried on-hand
    Water Quality Monitoring Equip.
    Field Screening Equip. (PID)
    Sample Kits and Containers
  Avg Response Times, 4< hours
  Evaluate risks to human health and environment
  Identify sensitive receptors & Env. Impacts
    Develop plans to mitigate, sample, and remediate
    Soil, sediment, surface water, & ground water

## Slide 18: Response
CSX Hazmat Contractors
  Training Qualifications
    FOST
    Insured, financially stable, safety record, RRW Training, audit compliance, 40-hour Trained, Hazmat physicals, etc.
  Equipment carried on-hand
    ER Trailers
    Vac Trucks
    Heavy Equipment
    Other info

## Slide 19: Response
CSX Hazmat Contractors
  Avg Response Times 4< hours
  Capabilities
    Varies by contractor/consultant
      Wrecking
      Transfers
      Air/soil/water monitoring
    Works side-by-side with CSX Hazmat Team and Responders

## Slide 20: Response
Other CSX Contractors
  Crane Companies
  Animal Experts/Biologists
    Bee Keepers
    Ornithologist
  River Restoration Specialists
  Barge Companies

## Slide 21: Response
  CSX Risk Management Team
  Mission:
  Address the needs of anyone negatively impacted by CSX operations with diligence, integrity and respect

## Slide 22: Response
  CSX Risk Management Team
  Crisis Response
  Evacuations can be 10 homes to 1000’s
  Secure hotels, restaurants, pharmacies, clothing, etc.
  Set up direct billings at hospital for decontamination/chemical exposure complaints, etc.
  Animal shelters, boarding, vet care, feeding, etc.
  Set up Community Outreach Center
  Inconvenience payments, expenses, Property Damage (PD), Right of Entry, personal injury (PI), etc.
  Expand response with CSX employee volunteers

## Slide 23: Response
  CSX Risk Management Team
  Past Incidents
  Mt. Carbon, WV – February 16, 2015
  Derailment, broken rail, 27 cars, crude oil fire
  Only injury to Morris Bounds, house that burned to the ground
  Evacuated approximately 1,1000 residents
  Most people were out of their homes for 5 days, except for the Bounds Family
  Community Outreach Center (COC) open for 2 weeks, then mail-in forms
  Inconvenience payments, expenses, PD, Right of Entry, PI

## Slide 24: Response
  CSX Risk Management Team
  Past Incidents
  Maryville, TN – July 1, 2015
  Derailment, tank car journal fire, acrylonitrile fire
  Evacuated approx. 5,000 residents
  Significant number of hotels & rooms
  Many people sent to hospital for decontamination, burning eyes and respiratory complaints
  Early contact with hospital, coordination & direct billing to CSX
  COC open for 10 days, then mail-in forms
  Inconvenience payments, expenses, PD, Right-of-Entry, PI

## Slide 25: Response
  CSX Risk Management Team
  Past Incidents
  Hyndman, PA – August 2, 2017
  Derailment, flat spots / build up on rail car from handbrake, 32 cars derailed, fire
  Evacuated 1,000 for 3 days, 25 households for 10 days and 2 households for 3 months
  Two Homes destoyed and CSX purchased those properties
  One legitimate PI, 4 claimed injuries, right-of-entry, PD, inconvenience
  COC open for 2 weeks, then mail-in forms

## Slide 26: Response
  CSX Risk Management Team
  Past Incidents
  Haverstraw, NY – April 14, 2023
  Sparks from CSX train started brush fires
  No injuries
  Evacuated 25 homes for a few hours
  No major structural Damage
  PD claims – fence, outbuilding and damaged tree claims

## Slide 27: Response
CSX Corporate Communications
  Serves as CSX PIO
  Handles media inquiries
  Contacted by :
    1-855-955-NEWS (6397)
    MediaTeam@csx.com

## Slide 28: Response
  Other Railroad Departments
  Engineering
    On-site throughout, preparing to route the derailment, track restoration,
    Signals
      Restoring signals, track equipment
    Bridges, Tunnels, & Structures
  Mechanical
    On-site throughout, re-railing, wreck clearing operations, staging wrecked calls

## Slide 29: ICS

## Slide 30: Response
Derailment
Hazmat Team Notified
Hazmat Team Responds and Evaluates the Incident
Environmental Group and LEADS Notified and Respond to the Incident
CSXT Derailment Team* Evaluates and Coordinates the Roles and Responsibilities
Senior HM Manager Oversees the Incident Management
Each Group Completes Roles and Responsibilities
Final Disposition/Closure Managed by Environmental Group

## Slide 31: Response
CSX Crews begin to show up – What to Expect? How to work together?
  Initial scene size-up
    Evaluating Resources
  Establishing contact with responders
    ICS – Set up Unified Command
  Develop a plan
  Implement Plan
    Directing Resources
  Re-evaluate
  Repeat

## Slide 32: Crew Entrapment
Notes: Crew Entrapment
What are the unique challenges associated with entrapped crew?
-Different types of locomotives and access points
-Where to cut if need be? How to cut?
-Dangers to First Responders

## Slide 33: Sights from large Derailments
Notes: Mt. Carbon, WV – 2015
During the Response Phase where would the responder fit in here?

## Slide 34: Incident Photos & Open Discussion

## Slide 35: Incident Photos & Open Discussion

## Slide 36: Incident Photos & Open Discussion

## Slide 37: Incident Photos & Open Discussion

## Slide 38: Phase 3 – Response, Incident Photos & Open Discussion

## Slide 39: Incident Photos & Open Discussion

## Slide 40: Incident Photos & Open Discussion

## Slide 41: Phase 4 - Recovery
Site Remediation
  Long Term
    What happens here?
    Cleaning & Wrecking of cars
    Environmental remediation and monitoring
      Soil & water sampling
      CSX Remediation Team
    What resources are used
      Cranes
      Torching Operations
      Vac Trucks
      Frac Tanks
  Where do responders fit in?
    Standby Operations

## Slide 42: Phase 4 - Recovery
Notes: Once the Emergency Response Phase is over, now begins the work on damaged / non-compliant rail cars.
Transfers, repairs, etc.

## Slide 43: Phase 4 - Recovery
Notes: Tank Cars being staged for cleaning and purging.
Tracks are open at this point.

## Slide 44: Phase 4 - Recovery
Notes: Waste is being stored for later off-site removal

## Slide 45: Phase 4 - Recovery
Notes: The CSX Remediation Team is on site long-term, handling environmental cleanup and restoration efforts