## Slide 1: ORSANCO Spill Response
Regional Response Team 4 Meeting
October 31 - November 1-2, 2023

## Slide 2: What is ORSANCO?
Ohio River Valley Water Sanitation Commission
    In 1920s and 1930s the Ohio River was very polluted
    Problem was too big for just one city or state to fix
    Created ORSANCO in 1948, bringing 8 states together to protect the river

## Slide 3: Ohio River Valley Water Sanitation Commission
Established by Compact (1948)
Ratified by Congress
Eight signatory states
  IL, IN, NY, KY,
  OH, PA, VA, WV

## Slide 4: ORSANCO Mission
Abatement of interstate water pollution in Ohio River Valley compact district.
Primary focus on Ohio River
Establish minimum WQ standards
Wastes discharged in one state shall not “injuriously affect” the waters of another state

## Slide 5: How the Commission Operates
3 Commissioners from each state
3 federal Commissioners
Funding
  States
  US EPA
22 person staff
Numerous inter-agency and stakeholder advisory committees

## Slide 6: What We Do
Our mission is to protect the uses of the Ohio River.
We monitor the river to assess if it is:
  Safe for drinking water
  Safe to recreate
  Safe to eat the fish
  Safe for aquatic life

## Slide 7: Keeping Our Drinking Water Safe
Drinking water source to 5 million people
Collect and analyze samples daily
Track major spills
Contact water intakes

## Slide 8: Is It Safe To Swim?
Collect and analyze samples for bacteria weekly during recreation season
Test samples for special events

## Slide 9: Can I Eat the Fish?
Collect and analyze fish samples every year.
Compare pollutant levels in fish to recommended values for food.

## Slide 10: Aquatic Life
Over 130 fish species identified in the Ohio River
Collect fish and bug population data yearly

## Slide 11: Role in Spill Response
Planning and Preparedness
Communications
Time-of-Travel Modeling
Water Quality Monitoring
Analytical Support

## Slide 12: Facilitating Emergency Response Preparedness
Emergency Response Focus Groups
  Engage federal/state/local ER personnel
  Upper Ohio (Marietta)
  Greater Cincinnati (Markland pool)
  Kentuckiana (Louisville to Evansville)
  Great Rivers Coordination Group (Paducah)
Water Users Advisory Committee
  Drinking water utilities

## Slide 13: Communications
Rotating 24/7 spill duty
  Receive spill reports via National Response Center (NRC) or direct calls
Facilitate interstate communication
  State and Federal Agencies
  Drinking Water Intakes
  Industrial Intakes
  Media / Elected Officials / General Public

## Slide 14: Spill Notification
Emergency Response Directory
  State/Federal contacts
  Water utilities
  Key river features
Spills Email Distribution List
Phone Notifications
  Water utilities and ER agencies
Coordinate Calls & Meetings
  Available to coordinate calls when necessary

## Slide 15: Key Questions?
What?
Where?
How much?
Actions taken?
Concentration?
When will it arrive at downstream intakes?
How long is the plume?

## Slide 16: Time-of-Travel Modeling
Ohio River Spill Modeling System
  Input date, time, amount, duration, decay
  Uses daily HEC-RAS flow file from NWS
Predicts plume time-of-travel
  Leading edge; peak; trailing edge
Estimates pollutant concentration
Utilized to:
  Inform water utilities and others of spill location
  Inform sampling crews where to monitor

## Slide 17: On-River Spill Tracking
Water quality sampling to track plume
  Shore-based (access points, locks & dams)
  Boat-based (safety limitations)
Provide coordination of multi-agency sampling efforts
Available Resources
  Boats – flow-through monitoring
  Multi-parameter datasondes
  Water and sediment samplers
  Flourometers
  Biological sampling

## Slide 18: Spill Detection Monitoring Network
Organics Detection System (ODS)
  Daily analysis of water samples for volatile organic compounds for spill detection
  16 stations (13 mainstem + 4 tribs)
  Detect thousands of compounds
  Calibrated for 30 VOCs
Provide coordination of laboratory services
  Within ODS network
  Contract laboratories
Gas Chromatograph Mass Spectrometer

## Slide 19
Organics Detection System Sites
Organics Detection System

## Slide 20: ODS Network Functions
Routine screening and ambient monitoring at intakes
  Alert operators of events that may impact treatment
Enhanced monitoring capabilities during spill events
  Increase sampling frequency
  Perform confirmation analyses
  Provide analysis to assist plume tracking
  Develop methods for contaminant analysis
Foster improved communications and information sharing among water utilities

## Slide 21: Routine Monitoring
Samples collected and screened daily
  Not all plants have ODS operators on weekends
Samples typically from raw water line
  Represents water drawn into plant at intake depth
ODS operators notify ORSANCO if detection >2 ppb or distinct observable pattern of low level detections
Approximately 2,000 samples screened monthly from all sites in ODS network

## Slide 22: Points of Emphasis
Reinforce need for quick initial WQ assessment
  Decisions will be made regardless of data availability
  Get screening-level data quickly to decision-makers
Impacts can extend well beyond point of release
Organics Detection System Partners
  Can be great resource for quick screening results
  Utility network also helpful to share treatment info

## Slide 23: ORSANCO Role in East Palestine, Ohio Train Derailment (February 3, 2023)
Ohio River Valley Water Sanitation Commission (ORSANCO)

## Slide 24: Initial Report
Feb 3, 2023 – Train derails in East Palestine, OH at 20:55
  50 cars derailed (10 haz mat tankers)
NRC report received 23:12 indicating derailed cars on fire
  POTENTIAL RELEASE of unknown materials
Melissa Smith via AP

## Slide 25: Initial Details
Feb 4, 2023 –
  Fire ongoing, but reduced
  5 vinyl chloride tankers derailed (at least 2 engulfed)
  Other hazmat railcars also burned
  Unknown materials/quantities released
  Sulphur Run to Leslie Run impacted by runoff
  Fish kill observed
  Incident location is 19 stream miles to the Ohio River
  Enters Ohio River at ORM 39.6
ORSANCO notified water utilities from East Liverpool, OH to Weirton, WV
  Spill report emailed to distribution list
Melissa Smith via AP

## Slide 26: Many Unknowns
Feb 5, 2023 –
  Pressure buildup noted in vinyl chloride railcar
  Water quality sampling of nearby creeks underway
Feb 6, 2023
  Products being transported reported to include:
    Vinyl chloride
    Butyl acrylate
    Benzene residue
    Combustible liquids
  Volumes released unknown
  Unknown if materials will reach the Ohio River
  Weirton, WV ODS station running samples every 2 hours
Gene J. Puskar / AP

## Slide 27: First Detection in Ohio River
Feb 7, 2023 –
  ORSANCO briefs Technical Committee
    No detections at that time
    Shortly thereafter first detection observed
Butyl acrylate detected at Weirton in sample collected at 1600 on Feb 6
All surface water utilities from East Liverpool, OH to Wheeling, WV notified by phone of detections
ORSANCO water quality field crew mobilized
EPA Feb 7, 2023

## Slide 28: Initial Detection in Ohio River Weirton, WV Feb 6, 2023 at 1600

## Slide 29: First ORSANCO Crews Deployed
Feb 8, 2023 –
ORSANCO crew sampled Little Beaver Creek to Bellaire, OH
Samples collected in triplicate
  1 for local ODS
  1 for Greater Cincinnati Water Works
  1 for ORSANCO
Second crew deployed to Incident Command
Received train manifest
Ordered butyl acrylate standard

## Slide 30: Continued Monitoring
Feb 9-10, 2023 –
ORSANCO met with response agencies & RP at Command Center
Repeated similar sampling approach as done on Feb 8
  Little Beaver Creek to Wheeling+
  Samples run at Wheeling Water
WV water intakes shut down
  Needed 2 non-detects in finished to reopen
Feb 11 - ATSDR releases Health Guidance Values
  n-Butyl acrylate: 560 ug/L
  2-ethylhexyl acrylate: 500 ug/L

## Slide 31
February 10, 2023
Detection
Non-Detect
Ref | City | Mile Point | State | Date | Time | n-Butyl Acrylate (p/a)
1 | Grimms Bridge | Beaver 3.0 | OH | 2/10/2023 | 1350 | present
2 | Lock 57 Park | Beaver 0.2 | PA | 2/10/2023 | 1300 | present
3 | East Liverpool | 40.2 | OH | 2/10/2023 | 1420 | absent
 | Chester | 43.0 | OH | 2/10/2023 | 1125 | absent
6 | Steubenville | 65.3 | PA | 2/10/2023 | 1605 | present
 | Follansbee | 70.8 | OH | 2/10/2023 | 1300 | absent
 | Wheeling River Grab | 86.0 | WV | 2/10/2023 | 1600 | present
8 | Bellaire | 93.9 | WV | 2/10/2023 | 1715 | absent
 | Moundsville | 101.7 | WV | 2/10/2023 | 1750 | present
 | New Martinsville | 126.0 | WV | 2/10/2023 | 1900 | present
 | Sisterville | 137.2 | OH | 2/10/2023 | 1945 | present
Surface Grab Samples analyzed at Wheeling ODS; presence/absence

## Slide 32: Tracking Leading Edge
Feb 11-19, 2023 –
Transitioned sampling to tracking leading edge
  Sampled 50 to 120 miles per day
  Early on plume traveled ~25 miles/day
  Later, velocities increased to ~100 miles/day
Sample
Analyze
Model
Report
Plan

## Slide 33: Downstream Tracking Concludes
Feb 19-20, 2023 –
Fixed station sampling at Markland Locks & Dam
  Sampled every two hours from lockwall
  Samples analyzed by Louisville Water
Feb 21-22, 2023:
Fixed station sampling at Cannelton Locks & Dam
  Sampled every two hours from lockwall
  Samples analyzed by Evansville Water
All samples from Markland & Cannelton non-detect

## Slide 34: Extended WQ Monitoring
Feb 22-23, 2023 –
Partial loss of containment reported near derailment site
ORSANCO crew sampled morning of Feb 23
Low-level hits on Little Beaver Cr. and Leslie Run
  Butyl acrylate
  2-ethyl hexanol
  2 ethylhexyl acrylate
March-April
Coordinated water quality sampling and analysis with several water utilities along length of river
All results non-detect

## Slide 35: Incident Review Perspectives
View incident from different perspectives to improve future responses
20/20 Hindsight
What If Scenarios
What You Know, When You Know It

## Slide 36: Challenges and Lessons Learned
East Palestine Train Derailment

## Slide 37: Communication Challenges
Limited/inaccurate incident details during early stages
ORSANCO not privy to response agency reports
Flow of info slow in the beginning
Struggled to get a coordinated sampling plan
Misleading social media led to undue public alarm
Many do not understand nature of their drinking water source
Inundated with information requests
Intense interest from media, elected officials and general public
Consistent messaging on dioxin slow to develop

## Slide 38: Analytical Challenges
Initially unknown materials released
  What to test for?
Labs not calibrated for butyl acrylate and other compounds released
  Needed standards to calibrate
Unusual detections at Wheeling ODS
  Detections interspersed with non-detects
ODS capabilities and utility not understood by some agencies

## Slide 39: Data Challenges
Which data to distribute and publish?
  ODS screening vs GCWW
How to best report peaks less than PQL?
Consistent messaging with partners
Keeping up with sample info, mapping and analytical results
Connectivity issues with electronic devices

## Slide 40: Lessons Learned
Be proactive to post contact info and incident details online
Response agencies unfamiliar with key attributes of ODS network
  Prepare materials detailing ODS capabilities, applications, and limitations to share with response agencies
Develop spill response toolbox to standardized data collection/reporting and improve spill response readiness
Need common understanding among partners regarding data reporting
  Screening level vs certified results
  Reporting data for peaks <PQL ???

## Slide 41: Lessons Learned
Proactively determine need for Command Center engagement and water quality sampling
Staff resources stretched to limits
  Need more staff cross-training for necessary redundancy
  Sampling, GIS, data management, ODS, Incident Command, public info
SWIGs want to be on spill updates
Engage ATSDR early if unregulated materials involved
Keep task management groups small (e.g. sampling plan development)

## Slide 42: ORSANCO Spill Response Recap
ORSANCO is a unique entity with focus on water quality
  Role sometimes not widely understood
Not typically a first responder
  Notifications are automatic; Field response upon consultation
Provides coordination among response agencies and water utilities
Extensive WQ monitoring, modeling & analytical capabilities
Can provide rapid turnaround of WQ results
Constantly working to improve response capabilities
  Integrated data sharing
  Opportunities to maintain & upgrade equipment

## Slide 43: Questions or Comments?
Contact Information
Sam Dinkins
sdinkins@orsanco.org
513/231-7719